## Slide 1
2012.09.04
SSD 개발팀
F/W Update Guide

## Slide 2
F/W Update Guide
Secure Erase
( Hynix_SSD_Tool )
F/W Update Flow
F/W Update
( SKhynix_SSD_Firmware_Updater(Build 002) )
Secure Erase
( Hynix_SSD_Tool )

## Slide 3
F/W Update Guide
Run “Hinix_SSD_Tool”.
( If you have any important data in target drive, I recommend you Backup your
SSD Drive before you do “Secure Erase”)
Click the “Drive Scan”
0. Secure Erase
1

## Slide 4
F/W Update Guide
Select the target device
Click the “Secure Erase”
0. Secure Erase
2
3

## Slide 5
F/W Update Guide
If Secure Erase succeed, you can confirm the message “Complete”
0. Secure Erase

## Slide 6
F/W Update Guide
Select the Device which you want to update F/W.
( Please Confirm the Model and FW Version)
Select the check box after confirmation of “OK!!! READY!!!” in RESULT category.
1
1. Run the F/W Updater Tool and Select the Target

## Slide 7
F/W Update Guide
Click the “!!! SSD Firmware Update !!!!”
2
2. Run the Firmware Update

## Slide 8
F/W Update Guide
Select the SFC File and Open
( Please confirm capacity (STD120GB / STD128GB / STD240GB / STD256GB) )
3
3. Select the SFC File

## Slide 9
F/W Update Guide
Click “Yes”
4
4. Confirmation

## Slide 10
F/W Update Guide
Confirm the message “Update Complete!!!” and click “OK”
5
5. Update Finished

## Slide 11
F/W Update Guide
You can confirm the change of FW Version to “504”
After updating FW, Don’t forget to do Secure Erase again.
6. Confirmation of F/W Updating